## Slide 1: Lean operations
Johan Jordaan
MBAA812 – Operations Management

## Slide 2
Designing operations
Managing operations
Optimising operations
Introduction (1)
Product & service design (5)
Process strategy (7)
Supply chain management (11)
Inventory (12)
Theory of constraints (7)
Lean (16)
Maintenance
(17)
Forecasting (4)
Quality (6)
People in operations (10)
Planning (13)
Project management (3)
Operations Strategy (2)
Location (8)
Layout (9)
Scheduling (15)
MRP & ERP systems (14)
Classroom
Community
Workplace
MBAA812 Roadmap
Insight
Understanding
Application
Study School
1
2
3
4
5
6
7

## Slide 4: What is lean production?
Lean Production can be defined as an integrated set of activities designed to achieve high-volume production using minimal inventories (raw materials, work in process, and finished goods)
Lean Production also involves the elimination of waste in production effort
Lean Production also involves the timing of production resources (i.e., parts arrive at the next workstation “just in time”)
Good housekeeping (5 Ss)
Notes: 3

## Slide 5: The Toyota Production System
Based on two philosophies:
  1. Elimination of waste
  2. Respect for people
Notes: 5

## Slide 6: Elimination of Waste
Saw
Saw
Lathe
Press
Press
Grinder
Lathe
Lathe
Saw
Press
Heat Treat
Grinder
Press
Lathe
Grinder
Grinder
A
2
B
Saw
Heat Treat
Lathe
Saw
Lathe
Press
Lathe
1
Focused factory networks
Group technology
3. Quality at the source
4. JIT production
5. Uniform plant loading
6. Kanban production control system
7. Minimized setup times
Notes: 6
Lots of small specialised plants rather than one intergrated plant
See video
Stop process if something goes wrong TQM

## Slide 8: Respect for People
Level payrolls
Cooperative employee unions
Subcontractor networks
Bottom-round management style
Quality circles (Small Group Involvement Activities or SGIA’s)
Notes: 21

## Slide 9: The seven wastes
Over-processing
Over-production
Waiting
Defects
Inventory
Motion
Transport
(Talent)

## Slide 10: Video: Lean manufacturing cell
Lean manufacturing cell

## Slide 11: Implementing Lean
Link operations
Balance workstation capacities
Redesign layout for flow
Emphasize preventive maintenance
Reduce lot sizes
Reduce setup/changeover time
Notes: 23

## Slide 12: Lean in Services (Examples)
Organize Problem-Solving Groups
Upgrade Housekeeping
Upgrade Quality
Clarify Process Flows
Revise Equipment and Process Technologies
Level the Facility Load
Eliminate Unnecessary Activities
Reorganize Physical Configuration
Introduce Demand-Pull Scheduling
Develop Supplier Networks
Notes: 30

## Slide 13: The 5 Ss
Sort/segregate – when in doubt, throw it out
Simplify/straighten – methods analysis tools
Shine/sweep – clean daily
Standardize – remove variations from processes
Sustain/self-discipline – review work and recognize progress
Two additional Ss
Safety – build in good practices
Support/maintenance – reduce variability and unplanned downtime

## Slide 14: Remove Variability
JIT systems require managers to reduce variability caused by both internal and external factors
Variability is any deviation from the optimum process
Inventory hides variability
Less variability results in less waste

## Slide 15: Just-In-Time (JIT)
Powerful strategy for improving operations
Materials arrive where they are needed when they are needed
Identifying problems and driving out waste reduces costs and variability and improves throughput
Requires a meaningful buyer-supplier relationship

## Slide 16: Inventory
Inventory is at the minimum level necessary to keep operations running
JIT Inventory Tactics
Use a pull system to move inventory
Reduce lot sizes
Develop just-in-time delivery systems with suppliers
Deliver directly to point of use
Perform to schedule
Reduce setup time
Use group technology
Table 16.2

## Slide 17: Reduce Lot Sizes
Figure 16.4
200 –
100 –
Inventory
Time
Q2 When average order size = 100
average inventory is 50
Q1 When average order size = 200
average inventory is 100

## Slide 18: Lower Setup Costs
Figure 16.5
Sum of ordering and holding costs
Holding cost
Setup cost curves (S1, S2)
T1
S1
T2
S2
Cost
Lot size

## Slide 19: Quality
Strong relationship
  JIT cuts the cost of obtaining good quality because JIT exposes poor quality
  Because lead times are shorter, quality problems are exposed sooner
  Better quality means fewer buffers and allows simpler JIT systems to be used

## Slide 20
Individual Assignment
On the template, prepare a one-page summary of the theme
Make sure that I can determine whether you understand the contents from your summary
Prepare a one-page summary of how this issue is applied at your organisation
Prepare a one-page recommendation how this could be improved in your organisation
Download long and short assignment templates from eFundi
Long (Contact 4 & 7)
Combine all the themes for this contact in one MSWord document (.docx)
SAVE AS: (# is the contact session number)
If all the themes are just theory summaries, save the document as Surname-Name-StudNo-Ind#-short.docx (Example:
Trump-Donald-12345678-Ind1-short.docx).
If at least one theme is a long one (i.e. has an analysis), save the document as
Surname-Name-StudNo-Ind#-long.docx (Example:
Trump-Donald-12345678-Ind1-long.docx)
Did I cover all themes for this contact?
Yes
No
Did I cover all themes for this contact?
SAVE
SAVE
Submit on eFundi before midnight on the deadline (Wednesday night 23:55)
Yes
No
Long or short assignment?
Short (Contact 1,2,3,5 & 6)